## Slide 1: Driver communication between C5509A and Penta Linux on ZynQ

## Slide 2: Agendal
C5509A
ZynQ 7000 - SoC
McBSP and SPI
Solutions

## Slide 3: C5509A
Features
  Up to 3 Multichannel Buffered Serial Ports (McBSPs)
  Six-Channel Direct Memory Access (DMA) Controller
  4-Channel (BGA) or 2-Channel (LQFP) 10-Bit Successive Approximation A/D

## Slide 4: ZynQ 7000 - SoC
Core A9 & FPGA - Linux & RTOS
Features
  Two full-duplex SPI ports with three peripheral chip selects
  8-Channel DMA Controller
    Memory-to-memory
    memory-to-peripheral
    peripheral-to-memory
    scatter-gather transaction support
  Two 12-Bit Analog-to-Digital Converters
    On-chip voltage and temperature sensing
    Up to 17 external differential input channels
    One million samples per second maximum conversion rate
  DSP Blocks
    18 x 25 signed multiply
    48-bit adder/accumulator
    25-bit pre-adder
  Peripgerals
    2x UART, 2x CAN 2.0B, 2x I2C, 2x SPI, 4x 32b GPIO

## Slide 5: McBSP
Mulitichannel Buffered Serial Port
Standard protocol
The primary use for the McBSP is for audio interface purposes
The McBSP consists of a data path and a control path that connect to external devices.
Separate pins for transmission and reception communicate data to these external devices.
Direct interface to: SPI devices

## Slide 6: McBSP
6 lines
  clock transmit - CLKX
  clock receive- CLKR
  frame sync transmit - FSX
  frame sync receive - FSR
  Data transmit - DX
  Data receive - DR

## Slide 7: SPI
- 4 Lines

## Slide 8: Connection - McBSP as SPI Slave
DX --> MOSI
DR <-- MISO
CLKR <-- SCK
FSR <-- CS

## Slide 9: Connection - McBSP as SPI Master
DX --> MOSI
DR <-- MISO
CLKX --> SCK
FSX --> CS

## Slide 10: Connection - McBSP as Master

## Slide 11: Solutions
Communication between C5509A and ZynQ by SPI protocol.
Target:
  SPI driver on Linux kernel run in ZynQ.